EMEP/MSC-W model:
Structure and Technical aspects
2. Peter Wind
4. Oslo, 29th April 2019

---
Core usage:
Pollutants in Europe

---
Individual customization
- Default values are provided
- Most common usage are relatively easy to control
  - simulation dates
  - emissions reduction by countries,
  - 3D output of pollutants
- Less common applications require more efforts
  - New emission sources
  - Other grid/resolution/projection
  - Other meteorological input
  - Different chemical compounds and chemical processes
  - ...

---
EMEP model has three parts
- The fortran code (provided by us)
  - Modelization and algorithms to simulate physical processes
- The input data (provided by us, can be completed for own needs)
  - Meteorological data
  - Emission data
  - Landuse
  - ...Other input data
- config_emep.nml
  - A text file that you modify to steer what the model actually does

---
Main structure of the code
- Read grid properties, emissions, landuse and all other input data
- Initiate the different modules for these data
- Time loop over the requested period
  - Read new metdata
  - Advection and diffusion
  - Emissions
  - Chemistry
  - Deposition (wet and dry)
  - Output the requested concentrations

---
Main structure of the code (emep_Main.f90):
call GridRead
call SetLandUse
call Emissions
call Init_XXX
do while (.not. End_of_Run)
  if (newmonth) call BoundaryConditions
  call Meteoread
  call advecdiff
  call runchem
  call WrtChem
enddo

---
Structure of the code: details
- Grid projection and resolution are taken from meteorological input data.
- Vertical levels can be given separately in a file (Vertical_levels.txt)
- Many different emission sources (see User guide)
- Time loop: dt_advec = 5-30 minutes (resolution dependent)
  - Metdata every 3 hours + interpolation
  - 15 Chemistry loops every dt_advec

---
Input data, an essential part of the model:
- Meteorology
- Emissions (many types+time factors)
- Landuse
- Boundary Conditions
  Except for meteorology, all other input data can be set to a default value. The data will be interpolated to the model grid.

---
Resolution
- In principle the projection and resolution of the model are not limited
- Main supported projections:
  - Polar stereographic
  - Spherical (lon-lat)
  - Rotated spherical
  - Lambert conformal
- Scales from global (0.5° degree resolution), to regional at fine scales (1 km) have been used
- Gridsize up to 3600x1800 has been used

---
Parallelization:
- One processor does the computation for one geographical rectangle.
- The processors are exchanging information using MPI
- Communication is only required for Input/Output and advection
- For large grids, the model scales to over 1000 processors

---
Example 12 processors
CPU4 communicates with CPU 0, 5 and 8
CPU8
CPU9
CPU10
CPU11
CPU4
CPU5
CPU6
CPU7
CPU0
CPU1
CPU2
CPU3

---
How long time take a run:
- Typically one month simulation for the large EMEP01 grid (1200x520) on 512 CPU, takes ca. 2 hours.
- For large grids, the model scales to over 1000 processors
- Time will increase with:
  - Larger grid
  - Fewer processors
  - Finer resolution
  - Large output (3D, hourly...)
- 60% chemistry, 20% advection, 20% I/O + communication

---
Modules’ overview - I
Main: emep_Main.f90
Grid: Par_ml.f90, GridValues_ml.f90, InterpolationRoutines_ml.f90
Configuration: Config_module.f90
Emissions Anthropogenic
Emissions_ml.f90
EmisDef_ml.f90
EmisGet_ml.f90
Timefactors_ml.f90
Meteo
Met_ml.f90 (read-in, PBL, kz)
MetFields_ml.f90 (defs)
BLPhysics_ml.f90
CellMet_f90 (sets for grid cells + L, U*)
SubGrid_ml.f90 (stability, L, U*)
Micromet_ml.f90 (Ra for landuses)
SoilWater_ml.f90 (Sets deep soil water)
Emissions Natural
SeaSalt_ml.f90
DustProd_ml.f90
ForestFire_ml.f90
Volcanoes_ml.f90
Landuse
Landuse_ml.f90
LandDefs_ml.f90
Meteorologisk Institutt met.no

---
Modules’ overview - II
Atm. Transport
Advection_ml.f90
Convection_ml.f90
Chemistry
CM_Chem*.f90
Solver.f90 (2-step chem. solver)
CM_Reactions*.inc (gas/aqueuos irrever.)
My_Aerosols_ml.f90 (equilibrium)
--> MARS_ml.f90 (EQSAM_ml)
My_SOA_ml.f90
ChemFunctions_ml.f90
Dry Deposition
CM_DryDep.inc
DryDep_ml.f90 (Micromet_ml)
Rsurface_ml.f90
Aero_Vds_ml.f90
Wesely_ml.f90
MosaicOutputs_ml.f90
EcoSystems_ml.f90
Boundary/Initial Conditions
BoundaryConditions_ml.f90
ExternalBICs_ml.f90
Nest_ml.f90
Wet Deposition
Aqueous_n_WetDep_ml.f90
CM_WetDep.inc
Meteorologisk Institutt met.no

---
Modules’ overview - III
Input/Output
OutputChem_ml.f90
Output_hourly_ml.f90
NetCDF_ml.f90
Derived_ml.f90
MosaicOutputs_ml.f90
Io_Progs_ml.f90
Sites_ml.f90
Other
PhysicalConstants_ml.f90
Country_ml.f90
MassBudget_ml.f90
TimeDate_ml.f90
Units_ml.f90
Timings_ml.f90
Meteorologisk Institutt met.no

---
Computational requirements:
- Linux computer (Fedora, Ubuntu, ...)
- Fortran compiler (ifort (Intel), gfortran (Gnu)...)
- MPI library (OpenMPI,...)
- NetCDF library (version 4 or later)
- 2-4 GB memory
- 30 GB disk space (mainly for metdata)
  ⇨ In practice any linux PC will do!

---
Requirement details:
Compilation: use 8 bytes reals
  - ifort -r8
  - gfortran -fdefault-real-8
- Netcdf: by default uses compressed output (i.e. Netcdf4/hdf5 ). This can be switched off (in configuration file put NETCDF_COMPRESS_OUTPUT=F)

---
Grid flexibility:
How does it work?
- The grid properties (projection, resolution, size etc.) are read from the file defining the meteorological data. These must be written as attributes in the NetCDF file.
- The input data which are not in the right grid are automatically interpolated into the proper grid
- The model can read directly WRF output meteorology.
- Making new meteorological input data for other met model from scratch is easy in theory... but not in practice

---
Gridded data: Emissions
- Gridded input over extended Europe
  - global NetCDF set with 0.5° resolution available
- Forestfire (FINN or GFAS)
- Biogenic VOC
- Soil NOx
- Dust
- Lightning
- Aircraft
- DMS
- Ocean NH3
- Volcanoes
- Roaddust: Europe only

---
Hybrid vertical coordinates
- Defined with a set of constants, An and Bn
- Pressure at level n defined by
  Pn = An + Bn Psurface
- Terrain following lower levels (large B, small A)
- Pressure levels at high altitude (large A, small B)
- Levels can be defined differently from the meteorological levels

---
Future work
- The model is evolving constantly, much based on your feedback!
  ⇒ Peter.wind@met.no

---
config_emep.nml
- Standard fortran namelist
- Set all run parameters
- Set only the settings you are interested in, (reasonable defaults values are set for the others)
- Path to all input files can be set
- «Large» version available at
  /home/sm_petwi/emep_course/config_emep.nml_Large

---
Steer the model with config_emep.nml
- Start and end dates of the simulation
  - startdate = 2016,1,1,0
  - enddate = 2016,1,31,24
- Meteorological data to use (defines grid projection and resolution)
  - meteo = ’DataDir/GRID/meteoYYYYMMDD.nc’
- Restricted domain
  - RUNDOMAIN = 20, 70, 40, 90,
- Emissions to be included
  - emis_inputlist(1)%name = ’Emis_GLOB05_05.nc’
  - USES%FOREST_FIRES = T ...
- Fields to be outputted
  - OutputConcs = 'SO2' ,'ug' ,'2d','AIR_CONCS','SPEC' ,4,
- Nesting (boundary concentrations)
  - MODE_READ=’NHOUR’
  - template_read_BC = 'EMEP_IN.nc'
- More details in user guide and exercises!