Data-processing with Fimex
1. ADPC-workshop
2. 2014-11-11

---
Data-flow at MET Norway
    Visualization
    Diana
    Tseries
    Vcross
    Profiles
Model1
config
Postproc.
nco
cdo
...
Model2
config
Met. work.
Model3
config
fimex
Radar1
Verification
Obs1
Archive

---
CDM-building blocks: Variables, Dimensions, Attributes
ncdump -h /opdata/arome_norway25/t2m500yrKF00.nc
netcdf t2m500yrKF00 {
dimensions:
time = UNLIMITED ; // (67 currently)
longitude = 1060 ;
latitude = 3680 ;
variables:
float air_temperature_2m(time, latitude, longitude) ;
air_temperature_2m:standard_name = "air_temperature" ;
air_temperature_2m:units = "K" ;
double time(time) ;
time:standard_name = "time" ;
time:units = "seconds since 1970-01-01 00:00:00 +00:00" ;
float longitude(longitude) ;
longitude:units = "degrees_east" ;
float latitude(latitude) ;
latitude:units = "degrees_north" ;
// global attributes:
:Conventions = "CF-1.0" ;
:institution = "Norwegian Meteorological Institute, met.no" ;
}
Variables
Attributes
for variables
Dimension-variables

---
Investigate a file with ncdump
-h: header
-c: header + dimension-variables
-t: translate times to ISO-format
-s: file-structure
-v varname: variable-values
- Find out what is inside a file, f.e. gfs_0p25_20141108_00.nc
- Which timesteps are currently there?
- What are the geographical coordinates of the first data-point?
- What are the compression and chunk-sizes?
- What about the files on nomads: http://nomads.ncep.noaa.gov:9090/dods/gfs_0p25
- Check with ncview?
[Speaker Notes: Check ncdump at /opt/netcdf4.3.0/bin/ncdump Eventually put it in your path in .gnomerc / .bashrc: PATH=.:$HOME/bin:/opt/netcdf4.3.0/bin]

---
Fimex functionality
- MET-extension of NetCDF C-API to support additional data-formats
  - NetCDF 3+4 / OpENDAP
  - Grib + tables (configurations)
  - MetGM
  - NcML
  - WDB
  - ProRAD
- Functions to simplify interpretation of data (Conventions)
- Function to modify data
  - Re-projection/interpolation (time/horizontal/vertikal)
  - Merging of files
  - Extraction/subsetting of data
  - Accumulation/deaccumulation
  - Theta -> temp, ...

---
Programming philosophy
- Modules have the same set of basic functions
  - Push metadata
  - Pull data (only required data is read/transfered)
- Modules are compeletely independent from each other
- Order of modules can be changed
- Modules can be used more than once
Metadata push
Source
NetCDF
GRIB 1/2
ProRAD
...
Sink
NetCDF
GRIB 1/2
MetGM
...
Extractor
Interpolator
reprojection
Vertical-
Interpolator
Time-
Interpolator
Processor
NCML
Quality-
Extractor
Data pull
Merge = 2 Sources
+ Interpolator

---
Fimex source consists of 3 parts
fimex command-line:
fimex --input.file=test.nc --input.type=nc --input.config=myconfig.ncml
Diana setup-files:
m=model t=fimex format=netcdf
f=/disk1/file.nc config=my_config.ncml
Tseries:
DataFile=/disk1/file.nc
DataDescription=AROME-PP
DataType=netcdf
DataConfig=my_config.ncml
R:
io = mifi.reader.new(«netcdf»,
«/disk1/file.nc»,
«my_config.ncml»);

---
Fimex source
- config not necessary for netcdf files (self-descriptive)
- type not necessary if file has known appendix, e.g. .nc, .grib
- source is here both --input and --output
- at every step of the fimex-change, you can look at the contents with --*.printNcML
- Task: Have a look at your files

---
Grib-configuration
- Connect grib-ids to netcdf-variables
- Add metadata to netcdf-variables
...
<variables>
    <parameter name="air_pressure_at_sea_level" type="float">
        <grib1 indicatorOfParameter="151" gribTablesVersionNo="128" identificationOfOriginatingGeneratingCentre="98" typeOfLevel="1" levelNo="0"/>
        <attribute name="standard_name" value="air_pressure_at_sea_level" type="string" />
        <attribute name="units" value="Pa" type="string" />
    </parameter>
    <parameter name="surface_air_pressure" type="float">
        <grib1 indicatorOfParameter="134" gribTablesVersionNo="128" identificationOfOriginatingGeneratingCentre="98" typeOfLevel="1" levelNo="0"/>
        <attribute name="standard_name" value="surface_air_pressure" type="string" />
        <attribute name="units" value="Pa" type="string" />
    </parameter>
...
Task: check files under EC/data_myanmar with cdmGribReaderEC.xml

---
NcML – Editing files on demand
- http://www.unidata.ucar.edu/software/thredds/current/netcdf-java/ncml/
- Works with netcdf-java and Fimex based programs
- Xml-file used for
  - Change variables, attributes, dimensions
  - Change values
  - Combine/aggregate files
  - Generate files
  - To get a ncml-file start e.g.
  fimex --input.file=file.nc –input.printNcML=xxx.ncml
  - To apply it use:
  fimex --input.file=file.nc --ncml.config=xxx.ncml --output.file=OUT.nc –output.type=nc4
  - fimex (command-line) creates allways new files – might be slow – Fimex library can do so «on the fly» while reading (config-option)

---
<?xml version="1.0" encoding="UTF-8"?>
<netcdf xmlns="http://www.unidata.ucar.edu/namespaces/netcdf/ncml-2.2"
        xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
        xsi:schemaLocation="http://www.unidata.ucar.edu/namespaces/netcdf/ncml-2.2 http://www.unidata.ucar.edu/schemas/netcdf/ncml-2.2.xsd">
<dimension name="time" isUnlimited="true" />
<variable name="time">
  <attribute name="units" type="String" value="hours since 2013-10-22 00:00:00" />
  <values>1 2 3 4 5</values>
</variable>
<variable name="x">
  <attribute name="standard_name" orgName="std_nm" />
</variable>
<variable name="strike_probability" orgName="strPr">
</variable>
<remove type="variable" name="number_of_tracks" />
</netcdf>
Make time unlimited
Change time-unit and add values
Rename an attribute of x
Rename variable 'strPr' to strike_probability
Remove variable 'number_of_tracks

---
ncatted: NCO attribute editor
ncatted -h -a att_nm,var_nm,mode,att_typ,att_val FILE.nc [OUT.nc]
  - att_nm, var_nm (attribute / variable name)
    - var_nm can be omitted (all variables) or 'global'
  - mode: a = append to existing attributes value; c = create if attribute does not exists; d = delete; m = modifiy if exists; o = overwrite
  - att_typ: f=float, d=double, l=long, s=short, c=char, b=byte
  - -a: attribute description, multiple occurances allowed
  - -h: no history, otherwise ncatted will put the command into the file – useful for debugging, but not for production
Example:
ncatted -h -a Conventions,global,o,c,CF-1.0 test.nc
ncatted will modify the existing files (unless OUT.nc) – very fast

---
ncrename: NCO renaming
ncrename -h [-a old_name,new_name] [-d old_name,new_name]
[-v old_name,new_name] FILE.nc [OUT.nc]
- Rename attribute (-a), dimension (-d) and variable (-v) names
- use var_nm@att_nm to modify a special variables attributes, otherwise all attributes with that name will be changed
- . in front of old_name will not fail, if old_name not found
- Examples
  ncrename -h -a .Conv,Conven test.nc
  ncrename -h -d Yc,y test.nc
  ncrename -h -v Yc,y test.nc
- Very fast and dangerous without OUT.nc
- -d and -v on dimension-variable does not work in a single command (bug)

---
Task: fix variable names and attr.
- The files in EC/data_myanmar/nc4/myanmar_atmos_20141108_00.nc has variable air_temperature_0m instead of air_temperature_2m and long_name 'Surface Temperature', which should be 'Screen level temperature (T2M)'
- Fix it indirectly without changing the file (ncml)
- Fix the file (ncrename/ncatted)

---
Fimex: extract
--extract reduces the data of the CDM:
- High level operations (detect axis and reduce):
Remove Variables:
  --extract.removeVariable arg remove variables
  --extract.selectVariables arg select only those variables (+ auxilliary)
Cut out a rectangle:
  --extract.reduceDimension.name arg name of a dimension
  --extract.reduceDimension.start arg start position of the dimension
  --extract.reduceDimension.end arg end position of the dimension
  --extract.reduceTime.start arg start-time as iso-string
  --extract.reduceTime.end arg end-time by iso-string
  --extract.reduceVerticalAxis.unit arg unit of vertical axis to reduce
  --extract.reduceVerticalAxis.start arg start value of vertical axis
  --extract.reduceVerticalAxis.end arg end value of the vertical axis
  --extract.reduceToBoundingBox.south ...

---
Extract-example and fimex-config
fimex –input.file=input.nc \
--extract.reduceDimension.name=time \ --extract.reduceDimension.start=0 \ --extract.reduceDimension.end=2 --extract.selectVariables=x \ --extract.selectVariables=y \ --extract.selectVariables=temperature --extract.printNcML
And a extract.cfg file for the same:
[extract]
reduceDimension.name=time
reduceDimension.start=0
reduceDimension.end=2
# add a comment
selectVariables=x
selectVariables=y
selectVariables=temperature
and run:
fimex -c extract.cfg –input.file=input.nc --extact.printNcML
Single config-options can be overwritten by command-line options. fimex.cfg in current directory or $HOME will be read automatically!

---
Task:
- extract your capital in 4x4 bounding-box from the files
- extract mslp and z at 500hPa at one timestep from your files

---
New data (240 hours)
- copy from the memory-stick the data of your country to the nc4 directory:
- cd /mnt/data/ADPC/EC/data_myanmar/nc4/
- cp /media/XXXXX/Data2014_11_11/myanmar* .
- XXXXX depends on memory stick
- Updated Slides:
- cp /media/XXXXX/Data2014_11_11/fimex_ADPC.odp $HOME

---
Information from JMA about GSM
- 1.25-degree resolution: no use restriction
- 0.5 degree:
  - formal application
  - no re-distribution without permission
  - If your audience are Asian NMHS's, introducing it is highly appreciated.
  - http://www.wis-jma.go.jp/cms/gsm/

---
Fimex: Reprojection / Horizontal Interpolation
- Requirements:
  - Input Coordinate System with horizontal axes
  - Description of new horizontal layout, either:
    - Netcdf-template with latitude/longitude axes (CS)
    - Proj-Projection + axes (in degree or m)
      - proj -lp
- Projection Methods
  - nearestneighbor, bilinear, bicubic
    - Require input rectangular grid with named projection
    - Allow interpolation, also from vectors (continuous data)
    - Generally fastest methods
  - coord_nearestneighbor, coord_kdtree
    - Work with any data with known latitude/longitude coordinates
    - Find closest point in input, require extend of input cell (distanceOfInterest)

---
  - forward_max, forward_mean, forward_median, forward_sum
    - Translate input lat/lon to output-grid
    - Very fast, but likely to leave holes (unless reducing resolution)
    - Mass-conservative
    - Does not work with template-based reprojections
- Preprocessing, avoid holes due to coastlines:
  - fill2d(critx=0.01,cor=1.6,maxLoop=100)
  - creepfill2d(repeat=20,weight=2)
- Examples
[interpolate]
method = bilinear
projString = +proj=utm +zone=33 +ellps=WGS84
xAxisValues=0,500,...,x;relativeStart=0
yAxisValues=0,500,...,x;relativeStart=0
xAxisUnit = m
yAxisUnit = m

---
Latitude/Longitude values
- Below functions work only with nearestNeighbor, bilinear and bicubic methods
- Simple example:
- This will interpolate to the points at (60,10), (60,9), (60.1,9), (45.4,17)
[interpolate]
method = bilinear
latitudeValues = 60,60,60.123,45.4
longitudeValues = 10,9,9,17

---
Create vertical sondes
 myanmar_vcross.txt
       The met.no vertical-cross section definition file in the form
       NT, NLL, LAT1, LON1, LAT2, LON2, ..., 'NAME'
eg. 3, 1, 60.1, 9.95, 'Oslo'
       with
       NT number type, with 1 = i,j coordinates (not supported); 2 = x,y
       coordinates (not supported); 3 = lat,lon in degree with decimals; 4 =
       lat, lon in degree *100 + minutes; 0 means end of input
       NLL number of coordinates, should be > 1
       LAT1, LON1, ... coordinates
       NAME a name in ' ' to give the cross-section
       * as comment

---
Example running sondes/profile
perl ../../../fiMetVcrosser.pl vietnam_viCross.txt --interpolate.method=bilinear --input.file=vietnam_atmos_20141111_12.nc --output.file=vietnam_vcross_20141111_12.nc --output.type=nc4

---
Task: Profiles / Cross-sections
- Edit the file 'bangladesh_vcross.txt'
- Add
  - at least 1 station
  - at least 1 cross-section (eventuall with 3 points?)
- run fiMetVcrosser.pl
- Does the new file appear in diana?

---
Task: Advanced Interpolation
- Wind at 10m
- Pick your capitals coordinates
- Bilinear
- Output as nc4
- Use --debug as fimex-option. What about rotation of wind-vectors?
- Look at the file with ncdump
[Speaker Notes: fimex --input.file=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc --input.type=netcdf --extract.selectVariables=x_wind_10m --extract.selectVariables=y_wind_10m --extract.reduceToBoundingBox.south=58 --extract.reduceToBoundingBox.north=62 --extract.reduceToBoundingBox.east=12 --extract.reduceToBoundingBox.west=8 --output.file=out.nc --output.type=nc4 --interpolate.method=bilinear --interpolate.projString="+proj=latlon +R=6371000" --interpolate.xAxisValue=9,10,11 --interpolate.yAxisValue=59,60,61 --interpolate.xAxisUnit=degree --interpolate.yAxisUnit=degree --timeInterpolate.timeSpec="210,240,...,360;relativeUnit=minutes since 2014-01-23 10:15:00;unit=seconds since 1970-01-01 00:00:00"]

---
Advanced Interpolation Solution
fimex --input.file=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc --input.type=netcdf --extract.selectVariables=x_wind_10m --extract.selectVariables=y_wind_10m --extract.reduceToBoundingBox.south=58 --extract.reduceToBoundingBox.north=62 --extract.reduceToBoundingBox.east=12 --extract.reduceToBoundingBox.west=8 --output.file=out.nc --output.type=nc4 --interpolate.method=bilinear --interpolate.projString="+proj=latlon +R=6371000" --interpolate.xAxisValue=9,10,11 --interpolate.yAxisValue=59,60,61 --interpolate.xAxisUnit=degree --interpolate.yAxisUnit=degree --timeInterpolate.timeSpec="210,240,...,360;relativeUnit=minutes since 2014-01-23 10:15:00;unit=seconds since 1970-01-01 00:00:00"
fimex --input.file=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc --input.type=netcdf --extract.selectVariables=x_wind_10m --extract.selectVariables=y_wind_10m --extract.reduceToBoundingBox.south=58 --extract.reduceToBoundingBox.north=62 --extract.reduceToBoundingBox.east=12 --extract.reduceToBoundingBox.west=8 --output.file=out.nc --output.type=nc4 --interpolate.method=bilinear --interpolate.latitudeValues=60,59.7,61.1 --interpolate.longitudeValues=10,10.2,10.5 --timeInterpolate.timeSpec="210,240,...,360;relativeUnit=minutes since 2014-01-23 10:15:00;unit=seconds since 1970-01-01 00:00:00"

---
Fimex: Time interpolation
- Requires time-axis in coordinate system
- Example:
  [timeInterpolate]
  timeSpec=0,3,...,24;relativeUnit=hours since 2000-01-01 00:00:00;unit=seconds since 1970-01-01 00:00
- Description in Fimex-Docs
- Only linear time interpolation
- Will pick exact time if matches!

---
Vertical Interpolation
- Interpolation of vertical levels to height, depth (in m) or pressure (in hPa).
- Requires: xyzt-coordinate system
- Examples:
- Allows creation of 4D-pressure
- Allows conversion from theta → temp
- Most, but not all vertical-input types supported, no 'sigma' output-types
- Different approx. for v-interpols (standard-atmosphere)
[verticalInterpolate]
dataConversion = theta2T
dataConversion = add4Dpressure
method = linear
type = height
level1 = 0,50,100,250,500,750,1000,1250,1500,1750,2250,2750,3250,3750,4250,4750,5500,6500,7000,7500,8000,8500,9000,9500,10000,10500,11500,12500,13500,14500,15500,16500,17500,18500,20000
[verticalInterpolate]
method = linear
type = depth
level1 = 3,5,10,20,50

---
Task: Select a datasource and try to adapt to format for diana / tseries
- data you brought
- GFS: http://nomads.ncep.noaa.gov:9090/dods/gfs_0p25
- JMA, see disk

---
Fimex – quality-control
Mask data by flags
<?xml version="1.0" encoding="UTF-8"?>
<cdmQualityConfig>
<!-- apply an external land-mask to sea_surface_temperature -->
<variable name="sea_surface_temperature" fillValue="-999">
<status_flag_variable name="land_mask" file="land.dat" type="felt" config="felt2nc.xml">
<allowed_values use="all"/>
</status_flag_variable>
</variable>
<variable name="bla">
<status_flag_variable name="blub">
<allowed_values>1,2,...,6</allowed_values>
<!-- or config by highest valid or lowest valid or all valid values -->
<!-- highest and lowest will be retrieved per data-slice, not for the whole variable -->
<!-- <allowed_values use="(highest|lowest|all|min:xxx.x|max:xxx.x)" /> -->
</status_flag_variable>
</variable>
</cdmQualityConfig>

---
Task: Simple snow filter
- Show precipitation where air_temperature_2m < 1degC
- Datasource: http://thredds.met.no/thredds/catalog/arome25/catalog.html
- Output as nc4
- Use --debug as fimex-option.
- Look at the in ncview / ncview2
- Is it slow? Just use first 5 timesteps
- Rename precipitation to precipitation_amount_acc to precipitation_amount_acc_when_cold
  - --ncml.config

---
Simple snow filter: Solution
- fimex --input.file=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc --input.type=netcdf --extract.selectVariables=precipitation_amount_acc --output.file=out.nc --output.type=nc4 --qualityExtract.config=Documents/2014/NetCDF/cdmQualityConfig.xml --debug --extract.reduceDimension.name=time --extract.reduceDimension.start=0 –extract.reduceDimension.end=4 –ncml.config=renamePrecip.ncml
- <?xml version="1.0" encoding="UTF-8"?>
  <cdmQualityConfig>
  <variable name="precipitation_amount_acc">
  <status_flag_variable name="air_temperature_2m">
  <allowed_values use="max:274"/>
  </status_flag_variable>
  </variable>
  </cdmQualityConfig>

---
Fimex: Interpolate-merging
- Two model-inputs grids (EC + Arome), output should be another model-grid (e.g. Norkyst400), very similar to interpolation
- Testing stage
  --input.file=eraInt_mslWind10_198001.nc
  --output.file=/tmp/test.nc
  --merge.inner.file=METNO_CRDX-EUR44_HINDC_6h_1989-01.nc
  --merge.method=bilinear
  --merge.projString=+proj=stere +lon_0=58. +lat_ts=60. +lat_0=90. +R=6371000
  --merge.xAxisValues=-3988000,-3984000,...,-1672000
  --merge.yAxisValues=-2548000,-2544000,...,-232000
  --merge.xAxisUnit=m
  --merge.yAxisUnit=m
  --merge.smoothing=LINEAR(5,2)

---
Fimex: NcML aggregation
- Files can be joined along the unlimited dimension (joinExisting)
- Or variables can be put together (union)
<?xml version="1.0" encoding="UTF-8"?>
<netcdf xmlns="http://www.unidata.ucar.edu/namespaces/netcdf/ncml-2.2"
        xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">
<!-- same as above, but with scan -->
<aggregation type="joinExisting">
    <scan location="." regExp="joinExistingAgg\d+\.nc" />
</aggregation>
</netcdf>
<?xml version="1.0" encoding="UTF-8"?>
<netcdf xmlns="http://www.unidata.ucar.edu/namespaces/netcdf/ncml-2.2"
        xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">
<aggregation type="union">
    <netcdf location="joinExistingAgg1.nc" />
    <netcdf location="unionAgg2.nc3" />
</aggregation>
</netcdf>

---
NCO: file-aggregation
- ncrcat joins files along the unlimited dimension
  - Dimension except unlimited must match
  ncrcat -4 -O file1.nc file2.nc file3.nc out.nc
  - Creates a new file (-O) out.nc in -4 = netcdf4-classic format
  ncrcat -A file1.nc file2.nc file3.nc file1.nc
  - Append-mode (-A) does not really append but creates a temporary new file
- ncks can append variables together
  ncks -A AROME-pp-clouds.nc AROME-DEF-tmp.nc
  - Adds pp_clouds variables to template
  - Dimensions must match!
  - -v var_nm allows selection of variable-name
  - -d dim,[min][,[max] allows selection of dimension
dim,[min][,[max]

---
Fimex: Performance considerations
- Many fimex-operations are fast, bottlenecks are often
  - IO (disk / network performance)
  - Netcdf4 build-in compression (default gzip -3)
- CPU-bottlenecks might be avoided by parallelization, e.g.
  - -n 4 (4 CPU support) (only for fimex-operations, not IO or compression)
  - Parallel fimex-tasks to many files, join files at the end
- It is possible to fill a file with information e.g. along the unlimited (time) dimension
  - --output.fillFile

---
Tasks: merge and check performance
- Download the first 6 hours of air_temperature_2m of the last 4 model runs from http://thredds.met.no/thredds/catalog/arome25/catalog.html
- Time the operations of
  - --output.fillWriter
  - --ncml.config aggregation
  - ncrcat
- --output.config allows to configure compressionLevel
  - See /usr/share/fimex/cdmWriterConfig.xml
  - Try to change compression-settings (with netcdf4) to 1, 3, and 9
- Download air_temperature_2m and precipitation_amount_acc separately and merge them with ncml or ncks
  - Do you manage to merge with local file and one OpENDAP source?

---
Solutions
fimex --input.file=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc --input.type=netcdf --extract.reduceDimension.name=time --extract.reduceDimension.start=0 --extract.reduceDimension.end=5 --extract.selectVariables=air_temperature_2m --output.file=temp1.nc --output.type=nc4
fimex --input.file=temp2.nc --output.fillFile=temp1.nc
ncks -O -4 temp1.nc temp2.nc outtemp.nc
<?xml version="1.0" encoding="UTF-8"?>
<cdm_ncwriter_config>
<default filetype="netcdf4" compressionLevel="9" />
</cdm_ncwriter_config>
fimex --input.file=temp1.nc --output.file=out.nc --output.config=cdmWriterConfig.xml
ncks -A -v precipitation_amount_acc -d time,0,0 http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_06.nc temp.nc

---
Ncap2: NCO arithmetic processor
- Full-featured processing language
- ncap2 -s 'prs_mdp[time,lat,lon,lev]=P0*hyam+PS*hybm' in.nc out.nc
- -s invokes a script, here to generate a new variable
- Dimension in functions or left hand casts must be prefixed by a $ sign
  - temp_avg=temperature.avg($time)
  - time[$time] = {1,2,3,4,5}
- Attributes are written by var_nm@attr_nm syntax
  - global@Conventions=»CF-1.0»
  - temp@units=»K»
- Many functions like
  - Min, max, avg, rms, total,...
  - Reverse, permute
  - hard_rain = precipitation > 100
- Caveats: slightly unstable, sometimes huge memory consumption

---
Task: Hours above -10degC
- Data from e.g. http://thredds.met.no/thredds/catalog/arome25/catalog.html
- Generate a field showing number of hour today with air_temperature_2m > -10 (0-67)

---
Solution: Hours above -10deg
fimex –input.file	=http://thredds.met.no/thredds/dodsC/arome25/arome_norway_default2_5km_20140123_00.nc --extract.selectVariables=air_temperature_2m --extract.reduceDimension.name=time --extract.reduceDimension.start=0 --extract.reduceDimension.end=23 --output.file=out.nc --output.type=nc4
- Did you know the data-formats mailing list:
  - http://lists.met.no/pipermail/data-format/2013-August/000017.html
ncap2 -O -s 't2m_aggr=(air_temperature_2m > 263).total($time);' out.nc t2m_aggr.nc

---
Utskifting av bakgrunnsbilde:
Høyreklikk på lysbildet og velg «Slide» -> «Set Background Picture for Slide...»
Velg ønsket bilde og klikk «Open»