# BUFR observations in Diana
## Synop, Metar, Dribu, Ship
### Station
- id
  - 1001 WMO BLOCK NUMBER
  - 1002 WMO STATION NUMBER
  - 1005 BUOY/PLATFORM IDENTIFIER
  - 1011 SHIP OR MOBILE LAND STATION IDENTIFIER
  - 1063 ICAO LOCATION INDICATOR
- auto
  - 2001 TYPE OF STATION
### Time
- 4001 YEAR
- 4002 MONTH
- 4003 DAY
- 4004 HOUR
- 4005 MINUTE
### Position
- 5001 or 5002 LATITUDE DEGREE
- 6001 or 6002 LONGITUDE DEGREE
- 7001 HEIGHT OF STATION
### Misc
- 7032 HEIGHT OF SENSOR
- 04024 Time period or displacement hour
- 04025 Time period minute
### Pressure
Convert all values from Pa to hPa
- PPPP
  - 10051 PRESSURE REDUCED TO MEAN SEA LEVEL
- ppp
  - 10061 3 HOUR PRESSURE CHANGE
- a
  - 10063 CHARACTERISTIC OF PRESSURE TENDENCY
- PHPHPH
  - 10063 CHARACTERISTIC OF PRESSURE TENDENCY
- HHH
  - 010003 GEOPOTENTIAL
### Temperature
Convert all values from K to C
- TTT
  - 12004 DRY BULB TEMPERATURE AT 2M
  - 12101 DRY BULB TEMPERATURE:
    - if 12004 DRY BULB TEMPERATURE AT 2M not reported
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
- TdTdTd
  - 12006 DEW POINT TEMPERATURE AT 2M
  - 12103 DEW POINT TEMPERATURE:
    - if 12006 not reported
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
- TxTn (min/max temerature)
  - 12014 MAX TEMPERATURE AT 2M:
    - if 4004 HOUR is 18
  - 12111 MAX TEMPERATURE:
    - if 12014 MAX TEMPERATURE AT 2M not reported
    - and 4004 HOUR is 18
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
    - and 04024 TIME PERIOD is 12
    - and 04024 TIME DISPLACEMENT is 0
  - 12015 MIN TEMPERATURE AT 2M:
    - if 4004 HOUR is 06
  - 12112 MIN TEMPERATURE:
    - if 120145 MIN TEMPERATURE AT 2M not reported
    - and 4004 HOUR is 06
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
    - and 04024 TIME PERIOD is 12
    - and 04024 TIME DISPLACEMENT is 0
- TwTwTw
  - 22042 SEA/WATER TEMPERATURE
  - 22043 SEA/WATER TEMPERATURE
  - if 22042 SEA/WATER TEMPERATURE is not reported
  - and 07063 DEPTH BELOW SEA/WATER SURFACE is below ?m
### Visibility
- VV
  - 20001 HORIZONTAL VISIBILITY M
    - (Only if 07032 is below ..., not implemented yet)
### Precipitation
- RRR (at HOUR = 06 or HOUR = 18)
  - 13022 Total precipitation past 12 hour
    - if 4004 HOUR is 06 or 18
  - 13011 Total precipitation / total water equivalent of snow
    - if 13022 Total precipitation past 12 hour not reported
    - and 4004 HOUR is 06 or 18
    - and 04024 TIME PERIOD is 12
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m ???????????
- RRR (at HOUR = 00 or HOUR = 12)
  - 13021 Total precipitation past 6 hour
    - if 4004 HOUR is 00 or 12
  - 13011 Total precipitation / total water equivalent of snow
    - if 13021 Total precipitation past 12 hour not reported
    - and 4004 HOUR is 00 or 12
    - and 04024 TIME PERIOD is 6
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m ???????????
  - RRR (HOUR not equal to 00,06,12,18, any of the following)
    - 13023 Total precipitation past 24 hour
    - 13022 Total precipitation past 12 hour
    - 13021 Total precipitation past 6 hour
    - 13020 Total precipitation past 3 hour
    - 13019 Total precipitation past 1 hour
    - 13011 Total precipitation past / total water equivalent of snow
### Clouds
- N
  - 20010 CLOUD COVER (TOTAL)
- Nh
  - 20011 CLOUD AMOUNT (of low or middle clouds)
- Ch
  - 20012 CLOUD TYPE
- Cm
  - 20012 CLOUD TYPE
- Cl
  - 20012 CLOUD TYPE
- h
  - 20013 HEIGHT OF BASE OF CLOUD
- CAVOK
  - 020009 GENERAL WEATHER INDICATOR (TAF/METAR) is 2
- Clouds (Metar)
  - Based on the folowing
    - 20011 CLOUD AMOUNT
    - 20012 CLOUD TYPE
    - 20013 HEIGHT OF BASE OF CLOUD
### Present and past weather
- ww
  - 20003 PRESENT WEATHER if below 200
- W1
  - 20004 PAST WEATHER (1) if between 2 and 20
- W2
  - 20005 PAST WEATHER (2) if between 2 and 20
### Wind
- dd
  - 11011 WIND DIRECTION AT 10 M
  - 11001 WIND DIRECTION
    - if 11011 WIND DIRECTION AT 10 M not reported
    - and 7001 HEIGHT OF SENSOR is between 9m and 11m
    - and 04025 TIME PERIOD is 10
- ff
  - 11012 WIND DIRECTION AT 10 M
  - 11002 WIND DIRECTION
    - if 11012 WIND DIRECTION AT 10 M not reported
    - and 7001 HEIGHT OF SENSOR is between 9m and 11m
    - and 04025 TIME PERIOD is 10
- fxfx
  - 011042 MAXIMUM WIND SPEED (10 MIN MEAN WIND)
- 911ff
  - 011041 MAXIMUM WIND SPEED (GUSTS)
- dndndn
  - 011016 EXTREME COUNTERCLOCKWISE WIND DIRECTION OF A VARIABLE WIND
- dxdxdx
  - 011017 EXTREME CLOCKWISE WIND DIRECTIONOF A VARIABLE WIND
- fmfm
  - 011041 MAXIMUM WIND SPEED (GUSTS)
- dndndn
  - 011016 EXTREME COUNTERCLOCKWISE WIND DIRECTION OF A VARIABLE WIND
- dxdxdx
  - 011017 EXTREME CLOCKWISE WIND DIRECTIONOF A VARIABLE WIND
### Snow depth
- sss
  - 13013 Snow depth
  - 13218 IND. FOR SNOW-DEPTH-MEASUREMENT - DNMI less than 4 -> sss=0
  - 20062 STATE OF THE GROUND (WITH OR WITHOUT SNOW)
### Ship
- Id
  - 1011 SHIP OR MOBILE LAND STATION IDENTIFIER
- ds
  - 1012 DIRECTION OF MOTION OF MOVING OBSERVING PLATFORM
- vs
  - 1013 SPEED OF MOTION OF MOVING OBSERVING PLATFORM
### Waves
- PwaPwa
  - 022011 PERIOD OF WAVES
- HwaHwa
  - 022021 HEIGHT OF WAVES
- Pw1Pw1
  - 022013 PERIOD OF SWELL WAVES
    - first system of swell
- Hw1Hw1
  - 022013 PERIOD OF SWELL WAVES
    - first system of swell
- dw1dw1
  - 022003 DIRECTION OF SWELL WAVES
    - first system of swell
- s
  - 022061 STATE OF THE SEA
### Metar
- PHPHPHPH
  - 010052 ALTIMETER SETTING (QNH)
- CAVOK
  - 20009 GENERAL WEATHER INDICATOR == 2
- Dv
  - 5021 BEARING OR AZIMUTH, DEGREE
- ww
  - 020019 SIGNIFICANT RECENT WEATHER PHENOMENA
- REww
  - 020020 SIGNIFICANT RECENT WEATHER PHENOMENA
## Temp
### Station
- id
  - 1001 WMO BLOCK NUMBER
  - 1002 WMO STATION NUMBER
  - 1011 SHIP OR MOBILE LAND STATION IDENTIFIER
### Time
- 4001 YEAR
- 4002 MONTH
- 4003 DAY
- 4004 HOUR
- 4005 MINUTE
### Position
- 5001 or 5002 LATITUDE DEGREE
- 6001 or 6002 LONGITUDE DEGREE
- 7001 HEIGHT OF STATION
### Pressure
Convert all values from Pa to hPa
- PPPP
  - 007004 PRESSURE
- HHH
  - 010003 GEOPOTENTIAL
### Temperature
Convert all values from K to C
- TTT
  - 12001 or 12101 DRY BULB TEMPERATURE
- TdTdTd
  - 12003 or 12103 DEW POINT TEMPERATURE
### Wind
- dd
  - 11001 WIND DIRECTION
- ff
  - 11002 WIND DIRECTION