# BUFR observations in Diana
## Synop, Metar, Dribu, Ship
### Pressure
Convert all values from Pa to hPa
- PPPP
  - 10051 PRESSURE REDUCED TO MEAN SEA LEVEL
- ppp
  - 10061 3 HOUR PRESSURE CHANGE
- a
  - 10063 CHARACTERISTIC OF PRESSURE TENDENCY
- PHPHPH
  - 10063 CHARACTERISTIC OF PRESSURE TENDENCY
### Temperature
Convert all values from K to C
- TTT
  - 12004 DRY BULB TEMPERATURE AT 2M
  - 12101 DRY BULB TEMPERATURE:
    - if 12004 DRY BULB TEMPERATURE AT 2M not reported
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
- TdTdTd
  - 12006 DEW POINT TEMPERATURE AT 2M
  - 12103 DEW POINT TEMPERATURE:
    - if 12006 not reported
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
- TxTn (min/max temerature)
  - 12014 MAX TEMPERATURE AT 2M:
    - if 4004 HOUR is 18
  - 12111 MAX TEMPERATURE:
    - if 12014 MAX TEMPERATURE AT 2M not reported
    - and 4004 HOUR is 18
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
    - and 04024 TIME PERIOD is 12
    - and 04024 TIME DISPLACEMENT is 0
  - 12015 MIN TEMPERATURE AT 2M:
    - if 4004 HOUR is 06
  - 12112 MIN TEMPERATURE:
    - if 120145 MIN TEMPERATURE AT 2M not reported
    - and 4004 HOUR is 06
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m
    - and 04024 TIME PERIOD is 12
    - and 04024 TIME DISPLACEMENT is 0
### Visibility
- VV
  - 20001 HORIZONTAL VISIBILITY M
    - Only if 07032 is ???
### Precipitation
- RRR
  - 13022 Total precipitation past 12 hour
    - if 4004 HOUR is 06 or 18
  - 13011 Total precipitation / total water equivalent of snow
    - if 13022 Total precipitation past 12 hour not reported
    - and 4004 HOUR is 06 or 18
    - and 04024 TIME PERIOD is 12
    - and 7001 HEIGHT OF SENSOR is between 1.5m and 2.5m ???????????
### Clouds
- N
  - 20010 CLOUD COVER (TOTAL)
- Nh
  - 20011 CLOUD AMOUNT (of low or middle clouds)
- Ch
  - 20012 CLOUD TYPE
- Cm
  - 20012 CLOUD TYPE
- Cl
  - 20012 CLOUD TYPE
- h
  - 20013 HEIGHT OF BASE OF CLOUD
- CAVOK
  - 020009 GENERAL WEATHER INDICATOR (TAF/METAR) is 2
- Clouds (Metar)
  - Based on the folowing
    - 20011 CLOUD AMOUNT
    - 20012 CLOUD TYPE
    - 20013 HEIGHT OF BASE OF CLOUD
### Present and past weather
- ww
  - 20003 PRESENT WEATHER if below 200
- W1
  - 20004 PAST WEATHER (1) if between 2 and 20
- W2
  - 20005 PAST WEATHER (2) if between 2 and 20
### Wind