# QC1-1
## General description
The KVALOBS range control applies climatological test values, i.e. each station is attributed a set of values with upper and lower limits for each month.
Every station has a set of range limit values comprising six values for each month. The values are:
- Upper physical limit value
- Highest test threshold value
- High test threshold value
- Low test threshold value
- Lowest test threshold value
- Lower physical limit value
There are two kinds of observation. One is the physical parameters like for example wind speed measured in m/s. The other is code parameters, for example total cloudiness with valid integer values between 0 and 9. The climatological threshold values for the code parameters will be identical to upper and lower limit on valid codes.
The physical parameters will have their range limit values set in the following manner:
The upper and lower physical limit value will be identical to the limit values inherited from the current control system applied to messages from automatic stations.
The highest and lowest test threshold value is initially set to the highest and lowest value measured during the latest 10 years period. The high test threshold value is set equal to the highest test threshold value minus 10 per cent of the difference between the highest and lowest test threshold value. The low test threshold value is set equal to the lowest test threshold value plus 10 per cent of the difference between the highest and lowest test threshold value.
The exception from these rules are the parameter groups: temperature, air pressure and wind speed, and relative humidity and wind direction with fixed limit values, 0 - 100% and 0 - 360 degrees respectively for the two latest parameters (see below).
The range limit values are stored in the Kvalobs SVN archive. Because the physical limits are the same for all stations and months, these limit values are stored in a separate file with parameterid and associated limit values only. The other limit values are tabulated with seven columns as shown below. The detailed file contains column headers and rows as exemplified below:
Stationid	parameterid	month	highest	high	lowest	low
18700	173	1	1032.6	1023.4	940.2	949.4

The input to the Kvalobs database is a table with the same structure as the above. The table contains limit values for all stations (except automatic stations) in operation during the last 10 years. In total there is 914 stations. Only the physical parameters at each station is included in the table. The table then consists of some 100 000 rows.
New stations established reasonably close to an exisiting one will have applied the same limit values as the existing station. In other cases interpolation of limit values from near by stations will be used. The interpolation will be relatively simple taking into account the distance to existing stations and eventually the difference in elevation. When there is no existing station sufficiently close model data and for marine stations Hindcast data will be applied. The latter also applies to stations which are not included in the calculation described above because of deficient quality control as for example automatic stations.
##### Equipment specific control configuration
QC1 on automated snow depth measurements
QC1 on Geonor bucket content RA
##### Detailed QC1-1 rational
QC1-1 on temperature, air pressure and wind speed (rødmerket tekst viser siste endringer i dokumentet). Se ev hele dokumentet nedenfor.
Kvalobs range control (QC1-1) on relative humidity (UU)
# station_param & checks
### station_param
kvalobs=# select count(*) from station_param where qcx ~ 'QC1-1' and stationid=0;
count
-------
   361
(1 row)
kvalobs=# select count(*) from station_param where qcx ~ 'QC1-1' and stationid<>0;
count
--------
565522
(1 row)
select count(*) from station_param where qcx ~ 'QC1-1';
count
--------
565883
(1 row)
### checks
kvalobs=# select count(*) from checks where qcx ~ 'QC1-1' and stationid=0;
count
-------
   358
(1 row)
kvalobs=# select count(*) from checks where qcx ~ 'QC1-1' and stationid<>0;
count
-------
     0
(1 row)
kvalobs=> select distinct checkname from checks where qcx ~ 'QC1-1' and NOT checkname='RANGE_CHECK' order by checkname;
        checkname
---------------------------
humidity_range
logger_t
qsi_range
Range-Check-110-Adapt-Acc
range_check_direction
Range-Check-EE-Codevalues
range_clock
(7 rows)
kvalobs=> select paramid,count(distinct qcx) from station_param where qcx in (select qcx from checks where qcx ~ 'QC1-1') group by paramid having count(distinct qcx)>1;
paramid | count
---------+-------
(0 rows)
### Result
From the last select above: There does not exist parameters with more than one qcx
&
2 different algorithms can not have the same qcx, that is different qcx implies different algorithms
=> There does not exist parameters with more than one algorithm.
## RANGE_CHECK is the main algorithm
##### Source code:
https://gitlab.met.no/obs/kvalobs/kvoss_intern/blob/master/kvmeta/algorithms/RANGE_CHECK.pl
##### Flag document:
https://wiki.met.no/kvalobs/kvalobs/kvalobs-flagg#grenseverdikontroll_range
## The other algorithms with metadata
./kvmeta_analysis.sh "select distinct checkname from checks where qcx ~ 'QC1-1' and checkname <> 'RANGE_CHECK' order by checkname"
All the metadata including the algorithms are under https://gitlab.met.no/obs/kvalobs/kvoss_intern/tree/master/kvmeta or under the directory $METADIR on a computer.
The script kvmeta_analysis.sh is found here: https://gitlab.met.no/obs/kvalobs/kvoss_intern/blob/master/kvmeta_analysis/kvmeta_analysis.sh
### humidity_range
algorithms/humidity_range.pl
##### QC1-1-263h
checks/checks_manual/QC1_rest/QC1-1-263h_checks.pl
station_param/station_param_manual/QC1_rest/263h_station_param.pl
##### QC1-1-262h
checks/checks_manual/QC1_rest/QC1-1-262h_checks.pl
station_param/station_param_manual/QC1_rest/262h_station_param.pl
##### QC1-1-264h
checks/checks_manual/QC1_rest/QC1-1-264h_checks.pl
station_param/station_param_manual/QC1_rest/264h_station_param.pl
##### QC1-1-265h
checks/checks_manual/QC1_rest/QC1-1-265h_checks.pl
station_param/station_param_manual/QC1_rest/265h_station_param.pl
### logger_t
algorithms/logger_t.pl
##### QC1-1-1x
checks/checks_manual/QC1_rest/QC1-1-1x_checks.pl
station_param/station_param_manual/QC1_rest/1x_station_param.pl
##### QC1-1-106x
checks/checks_manual/QC1_rest/QC1-1-106x_checks.pl
station_param/station_param_manual/QC1_rest/106x_station_param.pl
##### QC1-1-61x
checks/checks_manual/QC1_rest/QC1-1-61x_checks.pl
station_param/station_param_manual/QC1_rest/61x_station_param.pl
station_param/station_param_manual/QC1_rest/61x_s1_station_param.pl
##### QC1-1-81x
checks/checks_manual/QC1_rest/QC1-1-81x_checks.pl
station_param/station_param_manual/QC1_rest/81x_s1_station_param.pl
station_param/station_param_manual/QC1_rest/81x_station_param.pl
##### QC1-1-112x
checks/checks_manual/QC1_rest/QC1-1-112x_checks.pl
station_param/station_param_manual/QC1_rest/112x_station_param.pl
##### QC1-1-81x_s1
checks/checks_manual/QC1_rest/QC1-1-81x_s1_checks.pl
station_param/station_param_manual/QC1_rest/81x_s1_station_param.pl
##### QC1-1-15x
checks/checks_manual/QC1_rest/QC1-1-15x_checks.pl
station_param/station_param_manual/QC1_rest/15x_station_param.pl
##### QC1-1-175x
checks/checks_manual/QC1_rest/QC1-1-175x_checks.pl
station_param/station_param_manual/QC1_rest/175x_station_param.pl
##### QC1-1-213x
checks/checks_manual/QC1_rest/QC1-1-213x_checks.pl
station_param/station_param_manual/QC1_rest/213x_s1_station_param.pl
station_param/station_param_manual/QC1_rest/213x_station_param.pl
##### QC1-1-211x
checks/checks_manual/QC1_rest/QC1-1-211x_checks.pl
station_param/station_param_manual/QC1_rest/211x_station_param.pl
station_param/station_param_manual/QC1_rest/211x_s1_station_param.pl
##### QC1-1-176x
checks/checks_manual/QC1_rest/QC1-1-176x_checks.pl
station_param/station_param_manual/QC1_rest/176x_station_param.pl
##### QC1-1-107x
checks/checks_manual/QC1_rest/QC1-1-107x_checks.pl
station_param/station_param_manual/QC1_rest/107x_station_param.pl
##### QC1-1-73x
checks/checks_manual/QC1_rest/QC1-1-73x_checks.pl
station_param/station_param_manual/QC1_rest/73x_station_param.pl
##### QC1-1-56x
checks/checks_manual/QC1_rest/QC1-1-56x_checks.pl
station_param/station_param_manual/QC1_rest/56x_station_param.pl
##### QC1-1-110x
checks/checks_manual/QC1_rest/QC1-1-110x_checks.pl
station_param/station_param_manual/QC1_rest/110x_station_param.pl
##### QC1-1-217x
checks/checks_manual/QC1_rest/QC1-1-217x_checks.pl
station_param/station_param_manual/QC1_rest/217x_station_param.pl
##### QC1-1-49x
checks/checks_manual/QC1_rest/QC1-1-49x_checks.pl
station_param/station_param_manual/QC1_rest/49x_station_param.pl
##### QC1-1-84x
checks/checks_manual/QC1_rest/QC1-1-84x_checks.pl
station_param/station_param_manual/QC1_rest/84x_station_param.pl
##### QC1-1-109x
checks/checks_manual/QC1_rest/QC1-1-109x_checks.pl
station_param/station_param_manual/QC1_rest/109x_station_param.pl
##### QC1-1-172x
checks/checks_manual/QC1_rest/QC1-1-172x_checks.pl
station_param/station_param_manual/QC1_rest/172x_station_param.pl
##### QC1-1-61x_s1
checks/checks_manual/QC1_rest/QC1-1-61x_s1_checks.pl
station_param/station_param_manual/QC1_rest/61x_s1_station_param.pl
##### QC1-1-211x_s1
checks/checks_manual/QC1_rest/QC1-1-211x_s1_checks.pl
station_param/station_param_manual/QC1_rest/211x_s1_station_param.pl
##### QC1-1-215x
checks/checks_manual/QC1_rest/QC1-1-215x_checks.pl
station_param/station_param_manual/QC1_rest/215x_station_param.pl
##### QC1-1-87x
checks/checks_manual/QC1_rest/QC1-1-87x_checks.pl
station_param/station_param_manual/QC1_rest/87x_station_param.pl
##### QC1-1-271x
checks/checks_manual/QC1_rest/QC1-1-271x_checks.pl
station_param/station_param_manual/QC1_rest/271x_station_param.pl
##### QC1-1-214x
checks/checks_manual/QC1_rest/QC1-1-214x_checks.pl
station_param/station_param_manual/QC1_rest/214x_station_param.pl
##### QC1-1-173x
checks/checks_manual/QC1_rest/QC1-1-173x_checks.pl
station_param/station_param_manual/QC1_rest/173x_station_param.pl
##### QC1-1-216x
checks/checks_manual/QC1_rest/QC1-1-216x_checks.pl
station_param/station_param_manual/QC1_rest/216x_station_param.pl
##### QC1-1-90x
checks/checks_manual/QC1_rest/QC1-1-90x_checks.pl
station_param/station_param_manual/QC1_rest/90x_station_param.pl
##### QC1-1-262x
checks/checks_manual/QC1_rest/QC1-1-262x_checks.pl
station_param/station_param_manual/QC1_rest/262x_station_param.pl
##### QC1-1-178x
checks/checks_manual/QC1_rest/QC1-1-178x_checks.pl
station_param/station_param_manual/QC1_rest/178x_station_param.pl
##### QC1-1-104x
checks/checks_manual/QC1_rest/QC1-1-104x_checks.pl
station_param/station_param_manual/QC1_rest/104x_station_param.pl
##### QC1-1-213x_s1
checks/checks_manual/QC1_rest/QC1-1-213x_s1_checks.pl
station_param/station_param_manual/QC1_rest/213x_s1_station_param.pl
##### QC1-1-123x
checks/checks_manual/QC1_rest/QC1-1-123x_checks.pl
station_param/station_param_manual/QC1_rest/123x_station_param.pl
##### QC1-1-108x
checks/checks_manual/QC1_rest/QC1-1-108x_checks.pl
station_param/station_param_manual/QC1_rest/108x_station_param.pl
##### QC1-1-177x
checks/checks_manual/QC1_rest/QC1-1-177x_checks.pl
station_param/station_param_manual/QC1_rest/177x_station_param.pl
### qsi_range
algorithms/qsi_range.pl
##### QC1-1-208h
checks/checks_manual/QC1_rest/QC1-1-208h_checks.pl
station_param/station_param_manual/QC1_rest/208h_station_param.pl
##### QC1-1-2074h
checks/checks_manual/QC1_rest/QC1-1-2074h_checks.pl
station_param/station_param_manual/QC1_rest/2074h_station_param.pl
##### QC1-1-2070h
checks/checks_manual/QC1_rest/QC1-1-2070h_checks.pl
station_param/station_param_manual/QC1_rest/2070h_station_param.pl
##### QC1-1-2071h
checks/checks_manual/QC1_rest/QC1-1-2071h_checks.pl
station_param/station_param_manual/QC1_rest/2071h_station_param.pl
##### QC1-1-2073h
checks/checks_manual/QC1_rest/QC1-1-2073h_checks.pl
station_param/station_param_manual/QC1_rest/2073h_station_param.pl
##### QC1-1-2072h
checks/checks_manual/QC1_rest/QC1-1-2072h_checks.pl
station_param/station_param_manual/QC1_rest/2072h_station_param.pl
##### QC1-1-2075h
checks/checks_manual/QC1_rest/QC1-1-2075h_checks.pl
station_param/station_param_manual/QC1_rest/2075h_station_param.pl
### Range-Check-110-Adapt-Acc
algorithms/Range-Check-110-Adapt-Acc.pl
##### QC1-1-110b
checks/checks_manual/QC1_rest/QC1-1-110b_checks
station_param/station_param_manual/QC1_rest/110b_station_param
##### QC1-1-110a
checks/checks_manual/QC1_rest/QC1-1-110a_checks
station_param/station_param_manual/QC1_rest/110a_station_param
##### QC1-1-110c
checks/checks_manual/QC1_rest/QC1-1-110c_checks
station_param/station_param_manual/QC1_rest/110c_station_param
### range_check_direction
algorithms/range_check_direction.pl
##### QC1-1-64
checks/checks_manual/QC1_rest/QC1-1-64_checks
station_param/station_param_manual/QC1_rest/64_station_param
##### QC1-1-73
checks/checks_manual/QC1_rest/QC1-1-73_checks
station_param/station_param_manual/QC1_rest/73x_station_param.pl
station_param/station_param_manual/QC1_rest/73_station_param
##### QC1-1-75
checks/checks_manual/QC1_rest/QC1-1-75_checks
station_param/station_param_manual/QC1_rest/75_station_param
##### QC1-1-77
checks/checks_manual/QC1_rest/QC1-1-77_checks
station_param/station_param_manual/QC1_rest/77_station_param
##### QC1-1-63
checks/checks_manual/QC1_rest/QC1-1-63_checks
station_param/station_param_manual/QC1_rest/63_station_param
##### QC1-1-79
checks/checks_manual/QC1_rest/QC1-1-79_checks
station_param/station_param_manual/QC1_rest/79_station_param
##### QC1-1-76
checks/checks_manual/QC1_rest/QC1-1-76_checks
station_param/station_param_manual/QC1_rest/76_station_param
##### QC1-1-78
checks/checks_manual/QC1_rest/QC1-1-78_checks
station_param/station_param_manual/QC1_rest/78_station_param
##### QC1-1-61
checks/checks_manual/QC1_rest/QC1-1-61_checks
station_param/station_param_manual/QC1_rest/61x_station_param.pl
station_param/station_param_manual/QC1_rest/61x_s1_station_param.pl
station_param/station_param_manual/QC1_rest/61_station_param
##### QC1-1-62
checks/checks_manual/QC1_rest/QC1-1-62_checks
station_param/station_param_manual/QC1_rest/62_station_param
##### QC1-1-67
checks/checks_manual/QC1_rest/QC1-1-67_checks
station_param/station_param_manual/QC1_rest/67_station_param
##### QC1-1-80
checks/checks_manual/QC1_rest/QC1-1-80_checks
station_param/station_param_manual/QC1_rest/80_station_param
##### QC1-1-74
checks/checks_manual/QC1_rest/QC1-1-74_checks
station_param/station_param_manual/QC1_rest/74_station_param
### Range-Check-EE-Codevalues
algorithms/Range-Check-EE-Codevalues.pl
##### QC1-1-129a
checks/checks_manual/QC1_rest/QC1-1-129a_checks
station_param/station_param_manual/QC1_rest/129a_station_param
### range_clock
algorithms/range_clock.pl
##### QC1-1-1028
checks/checks_manual/QC1_rest/QC1-1-1028_checks.pl
##### QC1-1-1027
checks/checks_manual/QC1_rest/QC1-1-1027_checks.pl
## Flag document:
https://wiki.met.no/kvalobs/kvalobs/kvalobs-flagg#grenseverdikontroll_range
## Grenseverdikontrollen før metakvalobs
Grenseverdikontrollen før metakvalobs