# Redistribution of 24 hour precipitation
RR_24 is the precipitation collected over the last 24 hours. The Qc1 check precipcollected_flag identifies if an RR_24 value is valid (fd=1), erroneous (fd=3) or is the accumulation (fd=2) of a number (N) of consecutive 24 hour periods, where N>1. For the case fd=2, the accumulated value shall be distributed over the N 24 hours periods.
For each day the calculated
RR_24= model_value*observed_accumulation/sum_of_model_values
where the model values for the N missing values of RR_24 are calculated by an interpolation from the other stations making measurements at the same time and for which fd=1. At present, the interpolation uses an inverse 2-D squared distance weighting. Other weighting and interpolation techniques might be added later.
The calculated RR_24 updates the corrected value in the kvalobs database.
A warning is given if fmis=0 and original!=-1.
### Configuration and Parameters
The standard configuration options detailed in the user guide also apply to Redistribution.
Further configuration options are:
Option	Default	Description
endpoint_cflags	fmis=[04]&fd=2&fhqc=0	specify the flags for accumulation endpoints. Endpoints not matching these flags will not be detected
endpoint_uflags	no constraints
missingpoint_cflags	fmis=3&fd=2	specify the flags for the missing points before the accumulation
missingpoint_uflags	no constraints
neighbor_cflags	fd=1	specify requirements for the neighbor stations used for the interpolations. Neighbor stations that do not match these flags will be ignored.
neighbor_uflags	U2=0
warn_and_stop_cflags	fhqc=)0(	define for which flags for the accumulation point or the missing points before the accumulation the only action should be to print a warning and stop
warn_and_stop_uflags	no constraints
update_flagchange	fd=7;fmis=3->fmis=1	flags to change for the accumulation endpoint and the missing points
ParamId	---	selects the parameter ids to use. The only value tested here is 110 (RR_24).
tids	---	accepted typeids
measurement_hour	6	specifies the hour at which the data are expected. Series containing data with other times will be rejected with a warning.
min_neighbors	1	specifies the minimum number of neighbor stations with good data
max_neighbors	5	specifies the maximum number of neighbor stations to use
InterpolationDistance	100	radius in km inside which to search neighbor stations
warning_distance_closest_neighbor	50	minimum neighbor distance to print an INFO message about not so good neighbors
days_before_no_neighbor_warning	14	specifies the number of days after which a WARN is written to the logfile if there are not enough neighbor data
days_before_redistributing_zeroes_warning	14	specifies the number of days after which a WARN is written to the logfile if a non-dry accumulation has only dry neighbors

### Parameters
This algorithm has only been tested for paramid 110.
### Log Messages
There might be many different WARN messages in the log file /var/log/kvalobs/kvqc2d.log from this algorithm. These messages are (as of version 1.3.14pre3):
- original = missing/rejected for endpoint -- an endpoint (i.e. a row matching endpoint_?flags) has a missing original value; this might also indicate a row which somehow obtained the same flags as an endpoint.
- fmis=0 and original!=-1 for endpoint -- fmis should only be 0 for dry accumulations flagg-spec
- fd=2 and original!=corrected for endpoint -- redistribution has apparently been performed without setting fd=7
- endpoint matches warn_and_stop_flags or missing point ... matches warn_and_stop_flags for accumulation -- a row matches warn_and_stop_?flags, which is never by default
- missing point ... has different fd flag than endpoint -- a redistribution seems to have been done without setting fd flags consistenly
- missing point ... has fmis!=3 while fd=2 for endpoint -- normally, all missing rows (if they exist) should have fmis=3 before redistribution
- missing point ... has fmis!=1 while fd=7 for endpoint -- normally, all missing rows should have fmis=1 after redistribution
- found ... but expected ... rows with corrected values for accumulation ... -- normally, only one row should have a corrected value if the endpoint has fd=2, and all rows if fd=6/7
- redistributed sum ... starting ... differs from original in endpoint ... -- the sum of corrected values in the accumulation period does not match the original value in the endpoint row; unless fhqc!=0, an attempt will be made to fix this automatically
- fhqc mess for accumulation from .. to endpoint ... -- some rows in the accumulation period have fhqc=0, while others have fhqc!=0
- suspicious row ... before endpoint ..; giving up -- a row with missing original value has been found before the assumed accumulation period; to avoid a wrong redistribution in case the correct start date for the accumulation has not been detected, the algorithm stops
- no really good neighbors at obstime ... for accumulation ending ... -- the nearest neighbor is quite far away (more than warning_distance_closest_neighbor)
- accumulation ... > 0 would be redistributed to zeros for endpoint ... -- there is non-zero accumulated precipitation, but all accessible neighbor stations are dry so that the redistribution cannot be performed
- could not avoid difference of ... between distributed sum and accumulated value at endpoint ... -- some precipitation has been lost due to numerical (rounding) problems