# ALG004
## Acceptance Test for single point missing temperature values with TAN, TAX method
Step	Direction	Expected Result	Pass/Fail Criteria or Comment
001	Prepare test data in the test database.	--	--
	Download Test Data and gunzip.	--	--
	$ psql kvalobs	--	--
	DELETE FROM data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01';	--	--
	COPY data FROM '/home/kvalobs/alg004-kvalobsdb.dat' WITH DELIMITER AS '|';	--	--
	NB specify the actual path to the test data above as required.	--	--
		--	--
	Check that the time interval contains no Qc2 processed data:	--	--
	kvalobs=# select count(*) from data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01' and cfailed like '%Qc2%';	count=0	--
002	Download and gunzip alg004.cfg.gz to the /etc/kvalobs/Qc2Config directory and edit RunAtHour and RunAtMinute fields to the time that the test shall be run (e.g. a few minutes UTC in the future).	--	--
	The configuration by default has W_fhqc=0 and Wbool=true. The algorithm will only work on data that ha not been controlled by HQC	--	--

The configuration file also needs to be edited to include further flag controls ( -> ) and include this:
...
#Flag to set if value is corrected
S_ftime=1
change_fmis=3->1
change_fmis=0->4
...
003	Check log files to verify that the algorithm runs as scheduled, e.g. $ tail -f /var/log/Kvalobs/Qc2.log	--	--
004	Check that Qc2 processed data now resides in the database:	--	--
	kvalobs=# select count(*) from data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01' and cfailed like '%Qc2%';	count=55	--
005	Delete any existing data output (rm ALG004-Step5.dat) and then EXTRACT THE DATA:	DATA-S5	--

psql> select * from data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01' and cfailed like '%Qc2%' \g | cat >> ./ALG004-Step5.dat;
006	Plot the data. Download and use the two scripts ./unit_t_plot.bash and unitt.r.gz	--	--
	Make the bash file executable:	--	--
	chmod u+x unit_t_plot.bash	--	--
	Run the script	--	--
	./unit_t_plot.bash ALG004-Step5.dat		--
	and inspect the produced image ALG004-Step5.dat.jpg file.	--	--

Alternative to step 006 for use on dev-vm101
These files are already installed under /home/kvalobs.
As user kvalobs:
$ cd
$ ./unit_t_plot_manual.bash ALG004-Step5.dat
The data file ALG004-Step5.dat.XY.dat has been created ...
Now run the following commands in R:
--------------------------------------
FileName="ALG004-Step5.dat.XY.dat"
UTD <- read.table(FileName, header=TRUE)
pdf()
plot(UTD[,1],UTD[,2],ylim=c(-20,20),xlim=c(-20,20),xlab='Qc2 Algorithm/mm',ylab='Existing Correction/mm', main='200803 Hourly Temperature', sub='Missing Value Correction',col=4)
lines(c(-20,20),c(-20,20),col=3)
lines(c(-30,30),c(0,0))
lines(c(0,0),c(-30,30))
lines(c(-30,30),c(-30,30),col=3)
dev.off()
--------------------------------------
i.e. ... enter R:
$ R
...
> FileName="ALG004-Step5.dat.XY.dat"
> UTD <- read.table(FileName, header=TRUE)
> pdf()
> plot(UTD[,1],UTD[,2],ylim=c(-20,20),xlim=c(-20,20),xlab='Qc2 Algorithm/mm',ylab='Existing Correction/mm', main='200803 Hourly Temperature', sub='Missing Value Correction',col=4)
> lines(c(-20,20),c(-20,20),col=3)
> lines(c(-30,30),c(0,0))
> lines(c(0,0),c(-30,30))
> lines(c(-30,30),c(-30,30),col=3)
> dev.off()
>
> quit()
The above creates the file Rplots.pdf:
$ xpdf Rplots.pdf
NB if you have logged in using ssh -X kvalobs@dev-vm101 then the above will probably work!
007	Edit the configuration file and set Wbool=false. Rerun the algorithm. The algorithm will reprocess the data flagged as controlled by HQC already.	--	--
	kvalobs=# select count(*) from data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01' and cfailed like '%Qc2%';	count=121	--
	Capture the results. (rm ALG004-Step7.dat any previous test results)	DATA-S7	--

psql> select * from data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01' and cfailed like '%Qc2%' \g | cat >> ./ALG004-Step7.dat;
008	Plot results as in step 006 above.		--

Prerequisites
Set up the test data (these are prepatory notes for now for set up on pak)
Test Data comprising original data from 2008-03 with all the years set to 2024, the file only contains the parameters for the algorithm.
Configuration File
Setting-up or refreshing the database. (some database management may be required to stop page errors and the like ????, vacuum cleaning etc ???)
- $ psql kvalobs
- psql=> DELETE FROM data WHERE obstime BETWEEN '2024-02-28' AND '2024-04-01';
- psql=> COPY data FROM ./alg004-kvalobsdb.dat WITH DELIMITER AS '|';
Script for plotting the test results. See the Step # above: unit_t_plot.bash.gz
... and not to forget the corresponding R-script called by the shell script: unitt.r.gz