# QC2-OPE-MOD
Step	Direction	Expected Result	Pass/Fail Criteria or Comment
001	Set the $KVALOBS environement variable.	--	--
	e.g. for the dev-vm116 box:	--	--
	$export KVALOBS=/metno/kvalobs	--	--
002	Purge the configuration file directory.	--	--
	$rm $KVALOBS/Qc2Config/*.cfg	--	--
	Best to removing everything else in there as well!	--	--
003	Load the standard configuration file (currenty as below), e.g. for example:	--	--
	$cd $KVALOBS/Qc2Config	--	--
	$wget https://svn.met.no/kvoss/kvalobs/trunk/src/kvQc2/Reference/Redistribution.cfg	--	--
	$wget https://svn.met.no/kvoss/kvalobs/trunk/src/kvQc2/Reference/ProcessUnit.cfg	--	--
004	Edit the configurations files, specifically:	--	--
	RunAtHour and RunAtMinute, values to determine the schedulin	--	--
	LastNdays to determine the pocessing window.	--	--
005	Start Qc2 (see QC2-OPE-RUN)	--	--
	dev-vm116$ $KVALOBS/bin/kvstart	--	--
006	Let it run ...	--	--
	Monitor performance (e.g. database content, log files)	--	--
007	A stress test may be set up by defining many configuration files.	--	--

NOTES
- Add more configuration files to run the same algorithm more than once in the day
- Use cron and a script that toggles the “cfg” suffix to set up specific day algorithm