# Tseries Technical Documentation
## Description:
Tseries is an open-source time-series viewer for meteorological purposes. Tseries is developed and implemented at the Norwegian Meteorological Institute met.no, as a part of the operational meteorological workstation. Tseries can be used standalone, or in interaction with the Diana meteorological workstation. The Tseries package contains two programs:
1. tseries.bin is the timeseries viewer with a Graphical user interface
2. btseries is a batch version of Tseries, using the same graphical engine
The Goal of this Document is to explain the basic structure of Tseries setup- and stylefiles in order to adapt Tseries to a specific environment. The intended readership for this document is it-personnel and meteorologists, in charge of the operational setup of a local Tseries implementation. The description of the Tseries GUI is integrated in the applications help menu. The btseries user interface is described in the “btseries –help” option.
Styles and control are located in a separate package - The source code is downloadable at subversion
## Command line parameters:
Most of the input in Tseries is given by the control file, but can be overridden by command line input:
-s [ setupfile ]	if the setup file is not directly defined or invalid, Tseries will try to find a valid setup file with the name tseries.ctl in the system. First looking in the current directory, then in $HOME/.tseries/ and at last in /etc/tseries. If no valid setupfile exists, Tseries will exit.
-S [site]	site is just a short string. The user can define elements in the setup-file that are only used by certain groups. By this, several groups of users can share one setup-file to simplify maintenance.
-l [lang]	The language for the GUI. Can be configured in the GUI itself. Available languages are English(default), Norwegian Nynorsk, Norwegian Bokmål, Swedish, German, French. New languages can be added by using the qt-linguist tool.
-T [title]	Changes the window title, useful if you are running several instances of Tseries at the same time.
-H [wdbhost]	Host for the WDB connection
-u [wdbuser]	User for the WDB connection
-d [section1:key1=token1 section2:key2=token2]	The user can override any entity in the setup file by this option. Example: Use a different Diagrams definition file, without changing the setup file, by the option -d files:Defs=./tsDiagrams.def

## Datastreams:
There are several possibilities to add a Datastream to a Tseries Diagram:
1. HDF is the most common used datasource. In HDF all positions are predefined and named, Hdf input is defined in the base control file tseries.ctl. All HDF streams mentioned in tseries.ctl are indexed at startup. Streams from different HDF files can be combined in a single Diagram.
2. ASCII is implemented. But in an operational environment ASCII streams are space-consuming and ineffective. An example of usage of ASCII streams is presented in the appendix of this Document.
3. WDB the Weather and Water Database WDB is an open-source database system based on postgres. The system is developed at MET Norway. WDB is holding data as fields. Tseries retrieves interpolated timeseries from the database. As WDB interpolates data on-demand, WDB is more flexible, but slower than local HDF files. WDB is the dataengine for for the web-based, free weather service yr.no
4. KDVH is a MET Norway proprietary interface, based on URL. KDVH reads observations from the Norwegian climatic database. The Data are defined as Diagram entries in the control file (tseries.ctl) and can be implemented in any diagram.
Fimex Fimex is a library to process several datastream types (like NetCDF). Fimex Interpolates on demand from files. This is time-consuming, therefore fimexstreams are read for all positions on request. After that the Fimex stream is used from cache
## Diagrams:
A Diagram in Tseries consist of one or more datastreams connected to a given style. There are several files needed to generate a diagram: To generate a new diagram, one have to proceed the following workflow:
1. Create a new folder.
2. Copy a tseries.ctl and a tsDiagrams file into the folder.
3. Edit tseries.ctl. If the new diagram implements a new style and not a new stream, then just change the definition for Defs to the tsDiagrams file in this folder.
4. Copy a stylefile into the folder (for instance meteogram.style) rename the stylefile.
5. Edit tsDiagrams. Compose the parameters and models for the new diagram. Connect the diagram to the stylefile in this folder.
6. Edit the stylefile in this folder.
7. Start tseries.bin in this folder, the local tseries.ctl will be the default.
8. Repeat 6. and 7. until you are happy with the result.
## The Main Control file – tseries.ctl
The control file is split into several sections. All parameters given in the start of the file can be used as substitutes by $(parameter) anywhere later in the file. Unix Environment variables can be substituted by ${parameter}.
Single lines can be commented out by “#”
Keys, Sites and sections are “case-independent”
### Sites:
Tseries.ctl is a multi-user setup-file. To avoid the administration of several setup-files within one company, the file can contain several different configurations. The file is processed top-down. If a variable is defined several times, the last definition is valid.
Elements within sites in Tseries are usually inactive, the parser will ignore them, unless the user starts Tseries with the flag that defines the specific site ( the -S flag). A site is defined by a colon separated list of strings in square brackets. A site section ends by another site or a set of empty brackets.
Example:
server=meat.com
[FRUIT]
server=banana.com
[VEGETABLES:OTHERS]
server=potato.com
[]
Basically the server is defined as “meat.com”, if one wants to use the “banana.com” server, one have to start Tseries by: tseries -S FRUIT
To use potato.com in this example, one can start Tseries either with “ -S VEGETABLES” or “-S OTHERS”. This server is valid for for both flags.
### Sections
Sections are defined by chevrons like “<Path>”. A section is valid until the next section starts. Anything in tseries.ctl is organised in sections from the beginning of the first section. Entities written before the first section starts are pushed into a hash table and can be used freely as substitutes through the entire setup file.
Token	Description
nowTime	this special token can be used to generate a formatted string from the clock like nowTime=%d-%m

#### SECTION: <Path>
Token	Description
Etc	Path to find basic configurations
Images	Path to find images used in diagrams, like weather symbols
Lang	Path to find language files, Tseries looks for tseries_XX.qm files in this directory, where XX is the country code. .qm files are generated by the the Qt linguist tool.
Styles	Path to find stylefiles in tsDiagrams.def

#### SECTION: <Files>
Token	Description
Defs	The diagram definition file (tsDiagrams.def)
Configure	Autogenerated File to store configuration (like window size, language etc) from the GUI.
WeatherSymbols	The weather symbol definition file
stdImage	Image to send to Diana to show positions on the map
finImage	Image to display in Diana when the “find” button is triggered
iconImage	The Tseries icon
baseFilter	A filter file. By using the filter, Tseries will only display positions defined in the filter. The filter can be altered and saved locally by the user.
wdbBookmarks	In WDB mode one can store local bookmarks (positions) into this file
fimexBookmarks	In FIMEX mode one can store local bookmarks (positions) into this file
commonBookmarks	A file with common bookmarks, valid for all users

#### SECTION: <fimex>
Token	Description
FimexStreamTypes	List of streamtypes that will be read by Fimex , seperated by colon netcdf : ncml

#### SECTION: <WDB>
Token	Description
Host	The WDB host
User	The WDB User
busymovie	Animated gif to display that the server is busy - caching
readtime	If a request takes longer than readtime, the cache option appears ( in milliseconds )
maxRecord	Cutoff for records in bookmarks

#### SECTION: <klima>
Token	Description
url	base URL for the klima requequest
maxDistance	max distance to an observation in km (default=50)
maxObservationLength	how many hours to look into the past (default=300)

#### SECTION: <Server>
The server section is used to define the connection to Diana via coserver
Token	Description
Client	Name of the Client (Diana)
Name	Name that is sendt to the Client
Command	Command to start coserver

#### SECTION: <Streams>
The streams section is parsed by an older system, the pets graphical engine, on which Tseries is build. All data input from HDF files and Fimex streams is defined here, always the same way.
A new model starts with a collection name, this is kept for backwards-compatibility, these values are not used by Tseries
CollectionName=ECMeteogrammer
PreferredDiagram=Meteogram
InitialOpen=0
In a collection, any hdf/fimex file has to be registered the following way
##### A HDF/ASCII Stream
Token	Description
DataFile	The HDF file
DataDescription	The data description. A hdf file can contain several streams. You have to find the exact stream name in the file (when in doubt use vshow). The data description is used to define values in the diagram definition. (tsDiagrams.def)
DataType	HDF or ASCII
Contents	What parameter are defined in the file, x means any. The string is separated into four sections: Parameter,level,stream,runtime x,x,ECMWF,12 – means: All parameters from ECMWF, 12 x,x,ECMWF,x - All parameters from ECMWF, all times

##### A FIMEX Stream
Token	Description
DataFile	The datafile or URL (opendap) - use of glob is possible
DataDescription	The data description. Just a string to connect this stream to the diagram definition. (tsDiagrams.def)
DataType	[ type : tag ] type has to be defined in fimexStreamTypes, tag is optional. if no tag is given, tag=type. Tag is used to connect the parameterdescription to this stream
Contents	Not really used in Fimexstreams
DataConfig	Connect a Fimex config file (xml) to this stream

#### SECTION: <wdbParameter>
This section maps wdb parameters to tseries parameters

# tseries parameter = <wdb parameter> | <height> < height name> : <scale>
MSLP,0,x,x,APP= air pressure at sea level | 0 height above ground :/100
RR,0,x,x,APP= lwe precipitation rate | 0 height above ground
TT,0,x,x,APP= kalman air temperature | 2 height above ground :-273.15
UU,0,x,x,APP= x wind | 10 height above ground :*1.94384
#### SECTION:<WDBVECTORFUNCTIONS>
connect two parameters to a vector( to rotate them into a greografic grid)
UU,0,x,x,x :VV,0,x,x,x
#### SECTION: <klimaparameter>
# tseries parameter = klimaparameter
TT_O,0,x,OBS,x=TA
MSLP_O,0,x,OBS,x=PR
QNH_O,0,x,OBS,x=PH
#### SECTION: <klimanormals>
# tseries parameter = klimaparameter
# for these parameters, tseries has to build a timeline
TAM,0,x,OBS,x=TAM
TANM,0,x,OBS,x=TANM
TAXM,0,x,OBS,x=TAXM
#### SECTION: <fimexParameters>

tag = Given at the fimexstream definition (DataType : Tag)
fimexname = Request parametername
Unit = Udunits string
extradim = Predefined dimensions are time and position, height or similar has to
        be defined her for this particular parameter
# tseries parameter = tag | fimexname | Unit | extradim1 start1 len1 | extradim2 ...
#
#
MSLP,x,x,x = netcdf | air_pressure_at_sea_level | hPa | height 0 1
TT,x,x,x = netcdf | air_temperature_2m | Celsius
UU,x,x,x = netcdf | x_wind_10m | kt
# with a defined RRAC, tseries knows automatically how to extract RR from it
RRAC,x,x,x = netcdf | precipitation_amount_acc | kg/m^2
# Postprocessed temperature - alias...
TTPP,x,x,x = netcdf | air_temperature_2m | Celsius
## Wrf data
MSLP,x,x,x = wrf | air_pressure_at_sea_level | hPa
TT,x,x,x = wrf | T2 | Celsius
UU,x,x,x = wrf | U10 | kt |
VV,x,x,x = wrf | V10 | kt |
## The Diagram definition file – tsDiagrams.def
The Diagram definition file ties the streams to the actual diagram styles. One model input can appear in several diagrams, as well as several different models can use the same diagram type (like a meteogram). It is also possible to use one parameter from a defined stream into a certain diagram that is used by another stream. An example is the use of wind speed from an atmospheric model into a wave-diagram. Tseries builds its User interface based on this file. A stream appears first in the menus when it is defined here. If you want to remove a streams from Tseries, you have to remove it from this file as well. Otherwise it will appear as an empty entry in the menus.
#### The [models] section
All Models have to be defined in the models section, here one can change the display name of the model in the diagrams. The key has to be equal the stream name from tseries.ctl.
Example:
ECMWF=Ecmwf
ECMWF equals the DataDescription from tseries.ctl, Ecmwf will be displayed in the Tseries GUI menus
#### The Diagrams
Each diagram definition connects some parameters from some models to a style. A style can be used several times in different contexts. For instance is the S-meteogram (symbol meteogram) a diagram that uses the meteogram style, but it has also the weather parameter (WW) as input. Each diagram defintion starts with the [DIAGRAM] keyword and ends with the [ADD] keyword.
Examples:
# Standard meteogram
[DIAGRAM]
# The name of the diagram as it appears in the menu
NAME=Meteogram
# The connected style file
STYLEFILE=meteogram.style
# The streams connected to this diagram
[LEGALMODELS]
MODEL=ECMWF
MODEL=HARMONIE_2.5km
# Modelindependent = These parameters will be taken from
# all models, if available
[MODELINDEPENDENT]
PARAM=UU,x,x,x
PARAM=VV,x,x,x
PARAM=FF,x,x,x
PARAM=DD,x,x,x
[END]
# Modelspecific = These parameters are only used if they come from the specified model.
# Modelspecific values are not necessary part of the legalmodels.
# If they are not defined there, they will not occur in the menu
[MODELSPECIFIC]
MODEL=HARMONIE_2.5km
PARAM=TT_U,x,x,x
[END]
[MODELSPECIFIC]
MODEL=OBS
PARAM=TT,x,x,x
[END]
[ADD]
### Styles
Styles are defined in stylefiles. These are connected to data by tsDiagrams.def. By altering the stylesfiles you can control colors, line and object types in the diagram. There are hundreds of different types in a stylefile. You have to start with an existing stylefile and reduce that given stylefile until it fits your purpose. A style starts with the definition of the standard values: like default patterns, background color for the diagram etc.
#==================================================================
#
# Global settings
#
#==================================================================
bgColor= WHITE
topMargin= 50
bottomMargin= 50
leftMargin= 150
rightMargin= 150
# --------------------------------
# default values
type= DUM_PRIMITIVE
parameter= x,x,x,x
mother= DIAGRAM
plotAll= FALSE
enabled= TRUE
color= RED
color2= YELLOW
font= NORMAL
linePattern= FULL
fillPattern= SOLID
align= LEFT
spacing= MEDIUM
intSpacing= SMALL
label= TRUE
patternInColour= FALSE
lineWidth= 1.0
axisWidth= 2.0
tickWidth= 1.0
minRange= 0
interval= 1
delta= 2
minMargin= 0
maxIsSet= FALSE
minIsSet= FALSE
minValue= 100000
maxValue= -100000
yaid= 0
centerVector= FALSE
numTickMajor= 10
numTickMinor= 2
labelSpace= 120
quantized= FALSE
quantum= 1.0
gridxonly= FALSE
axisgrid= FALSE
gridwidth= 1
gridcolor= GREY25
gridstyle= DOTTED
[DEFAULT]
Then you have to define axes
first at least one x-axis
# --------------------------------
# utc-time
[NEW]
type= UTC
order= 8
height= 25
spacing= SMALL
font= NORMAL
color= BLUE
minSkipX= 15
[ADD]
And then several y-axes. A curve in the diagram is connected to an axis. If you want to display, for instance several temperatures, you have to create a temperature axis. Then you have to connect the curves to that axis. By that it is guaranteed that the curves are scaled correctly to each other. Each axis has an unique identifier (y-axis-id/yaid). Yaid is used to connect parameters to the axis.
# ----------------------------
# Yaxis (T2m)
[NEW]
type= YAXIS_STATIC
yaid= 0
delta= 1.0
interval= 0.5
minMargin= 0.25
minRange= 5.0
minIsSet= FALSE
maxIsSet= FALSE
text=
align= LEFT
axis= LEFTLEFT
color= RED
lineWidth= 2
linePattern= FULL
patternInColour=TRUE
[ADD]
With axis in place, you have to define a parameter and connect it to it. In this case, the curve is presented in 2 different colors, one for -100 to 0 degrees and one for 0-100 degrees.
[NEW]
type= LINE
yaid= 0
parameter= TT,0,x,x
text= T2m [°C]
lineWidth= 2
linePattern= FULL
patternInColour= FALSE
colorbyvalue= TRUE
datalimits= -100,0,100
colorlist= BLUE,RED
patternInColour= FALSE
[ADD]
#### Valid Types:
There are several types in Tseries that can be used by the different elements.
### Colors

Fillpatterns
DIAGRIGHT
DIAGLEFT
DIAGCROSS
HORIZONTAL
VERTICAL
SHORIZONTAL
SVERTICAL
SQUARE
SOLID

Linestyle
DASHED
DASHDOTTED
DASHDASHDOTTED
DOTTED